## Slide 1
The Imperative for Grid Cyber Resilience
Bill Sanders
April 23, 2018

## Slide 2: The Challenge: Provide Trustworthy Grid Operation in Possibly Hostile Environments
Be Trustworthy
  A system which does what is supposed to do, and nothing else
  Safety, availability, integrity, timeliness, confidentiality, …
Tolerate a Hostile Environment
  Accidental failures, design flaws, and malicious attacks
Consider the Cyber, Physical, and Social System Aspects
Provide Assurance through Assessment
  Provide justification that the system will operated as expected
  Choose among design alternatives to achieve greater trustworthiness

## Slide 3
Source: carol Hawk, DOE ceds overview presentation

## Slide 4: Cyber Security Facts (according to Sanders)
Grid cyber infrastructures are complex, and their complexity will only continue to increase.

## Slide 5: In the smart grid, the cyber Infrastructure must provide control at many levels and multiple dimensions
Multi-layer Control Loops
Multi-domain Control Loops
  Demand Response
  Wide-area Real-time control
  Distributed Electric Storage
  Distributed Generation
Intra-domain Control Loops
  Home controls for smart heating, cooling, appliances
  Home controls for distributed generation
  Utility distribution Automation
Resilient and Secure Control
  Secure and real-time communication substrate
  Integrity, authentication, confidentiality
  Trust and key management
  End-to-end Quality of Service
  Automated attack response systems
  Risk and security assessment
  Model-based, quantitative validation tools
Distribution and Generation
Transmission and Distribution
Generation and Transmission
Resilient and Secure Control Loops
Note: the underlying Smart Grid Architecture has been developed by EPRI/NIST.

## Slide 6: Cyber Security Facts (according to Sanders)
Grid cyber infrastructures are complex, and their complexity will only continue to increase.
Cyber infrastructures intended to be secure must operate through attacks.

## Slide 7: Cyber Security Facts (according to Sanders)
Grid cyber infrastructures are complex, and their complexity will only continue to increase.
Cyber infrastructures intended to be secure must operate through attacks.
Absolute cyber security is unattainable.

## Slide 8: A Decade of Energy Cyber Infrastructure Attack Malware
2010: Stuxnet: Targeted Siemans industrial control systems in Iran. Was first discovered malware that spies on and subverts industrial systems and the first to include a programmable logic controller (PLC) rootkit.
2014: Dragonfly/Havex: Focus was to collect ICS network and access control information. Evidence suggests this was provided to a well organized and funded group outside countries from which the data was collected.
2015: Black Energy 3: Used in attack on the Ukraine power grid. Considered to be the first known power grid cyberattack. Hackers were able to successfully compromise information systems of three energy distribution companies and temporarily disrupt electricity supply to the end consumers.
2016: CRASHOVERRIDE: Second known attack in Ukraine. Impacted a single transmission level substation. Significant increase in sophistication of attack code relative to past attacks.
2017: TRISIS/TRITON: Incident at a critical infrastructure organization which targeted Schneider Electric’s Triconex safety instrumented system (SIS) and where an attacker deployed malware which targeted systems provided emergency shutdown capability for industrial processes. Deployed against at least one victim in the Middle East.

## Slide 9: Potential Power-System-Specific Cyber Attack Strategies
Tripping breakers
Changing values breaker settings
  Lower settings can destabilize a system by inducing a large number of false trips
  Lowering trip settings can cause extraneous other breakers, causing overloading of other transmission lines and/or loss of system stability
Corrupting Control Information: Smart Meters, SCADA Data, PMU Data, Dispatch Information, etc.
Sophisticated lateral movement attacks
Life cycle attacks
Insider threats
Physical damage by cyber means
Combined physical and cyber attacks

## Slide 10: Lateral Movement in Cyber Kill Chain Demands Resiliency
Reconnaissance
Delivery
Command and Control
Lateral Movement
Goal Accomplishment
Port scanning
Media analysis
Spear phishing
Zero-day exploits
Control channels
Remote desktop
Privilege escalation
Data exfiltration
Physical damage
Source: http://about-threats.trendmicro.com/cloud-content/us/ent-primers/pdf/tlp_lateral_movement.pdf
During lateral movement:
Attacker moves laterally between hosts
Attacker uses remote desktop connections, SSH, Windows management inventory, administrator tools

## Slide 11: Lateral Movement Attack Examples
2009
2011
2013
2015
40 million credit card records stolen
Expected cost ~$248 million
80 million personal records stolen
Expected cost ~$115 million
Ukrainian
Power Grid
Power outage for about 6 hrs.
Affected ~225,000 consumers
Many companies and government agencies have experienced
lateral movement based attacks, leading to large-scale damages.

## Slide 12: Cyber Security Facts (according to Sanders)
Grid cyber infrastructures are complex, and their complexity will only continue to increase.
Cyber infrastructures intended to be secure must operate through attacks.
Absolute cyber security is unattainable.
Resiliency is key: Protect the best you can, but realize that perfect protection is impossible, so resiliency can only be achieved through tolerating attacks through online detection and response.

## Slide 13: Notional Architecture for Resiliency
”World View”
System Model
OFFLINE/ONLINE
COMPUTATION
Diverse System
Monitoring
Monitor Fusion
Response Selection and Actuation
ONLINE COMPUTATION
Monitor Placement
RESILIENCY
INFRASTRUCTURE
Secure Monitoring and Response Infrastructure

## Slide 14: Notional Architecture for Resiliency
”World View”
System Model
Diverse System
Monitoring
Monitor Fusion
Response Selection and Actuation
ONLINE COMPUTATION
Monitor Placement
RESILIENCY
INFRASTRUCTURE
Secure Monitoring and Response Infrastructure
The monitor placement algorithm deploys sensors according to specified monitoring goals
The system model represents the services, possible responses, attacker characteristics, and architecture of a system.
OFFLINE/ONLINE
COMPUTATION

## Slide 15: Notional Architecture for Resiliency
”World View”
System Model
Diverse System
Monitoring
Monitor Fusion
Response Selection and Actuation
ONLINE COMPUTATION
Monitor Placement
RESILIENCY
INFRASTRUCTURE
Secure Monitoring and Response Infrastructure
The sensor inputs, alerts, and logs feed into a different set of fusion and correlation algorithms to generate a higher-level alert
OFFLINE/ONLINE
COMPUTATION

## Slide 16: Notional Architecture for Resiliency
”World View”
System Model
Diverse System
Monitoring
Monitor Fusion
Response Selection and Actuation
ONLINE COMPUTATION
Monitor Placement
RESILIENCY
INFRASTRUCTURE
Secure Monitoring and Response Infrastructure
The decision algorithm decides on learning responses to intensify and focus the monitoring resources, and/or effect a response strategy, e.g.
  Block an attacker
  Move a target
  Reallocate services
  Recover services
OFFLINE/ONLINE
COMPUTATION

## Slide 17: Notional Architecture for Resiliency
”World View”
System Model
Diverse System
Monitoring
Monitor Fusion
Response Selection and Actuation
ONLINE COMPUTATION
Monitor Placement
RESILIENCY
INFRASTRUCTURE
Secure
Monitoring and Response Infrastructure
The monitoring and response architecture provides a trustworthy infrastructure on which to implement resiliency services and maintain a trustworthy world view.
OFFLINE/ONLINE
COMPUTATION

## Slide 18: Resiliency in Practice: Detecting Lateral Movement
Lateral movement chains
Internal and external NetFlow
Host-level activities
(e.g., sockets, files, and processes)
Compromised hosts
Network-wide hierarchical fusion
Unsupervised anomaly detection

## Slide 19: Hierarchical Fusion
Lateral Movement detection by fusing host-level process communication with network flow information
Process communication used to infer network flow correlation
Hierarchical fusion of events results in a chain of correlated connections that describes lateral movement in the system
Local inference of correlation events allows for fusion without the need for a global clock
A
C
S1
P1
P2
P3
P4
P5
S2
F
Host-view
T=1
T=3
T=4
T=5
T=6
T=0
Host
Process
Socket
Ahmed Fawaz, Atul Bohara, Carmen Cheh, and William H. Sanders. 2016, Lateral Movement Detection Using Distributed Data Fusion. In Proc. IEEE 35th Symposium on Reliable Distributed Systems pp. 21-30.
Notes: Current methods: Correlate NetFlow to detect lateral movement
Proposed method: Correlate between host-level system calls and network information across the system to generate system-wide lateral movement chain
Hierarchical Fusion: Process communication graph  Host communication graph  Group communication graph
Agent on each host: infers connection correlation using the Process Communication Graph
Collect timestamped events of:
Processes running
Process communication (pipes, messages,…)
Network connections (with a unique ID across system)
File access
The agent creates a timed directed graph of communication between processes
Correlation is inferred via a path between incoming and outgoing connections

## Slide 20: Malicious Lateral Movement via Machine Learning
Indicators | Anomalous external communication | Large number of divers LM chains
Insights | Communication with potential C&C servers will result in large number of distinct outward connections | Communication graph generated by normal hosts is sparse and significantly follows client-server model Benign chains are long as compared to attacker chains
Features | C_score E.g., number of connections to unique external domains | Number of LM chains Statistics on LM chain lengths: {mean, MAD, IQR, Range}
Atul Bohara, Mohammad A. Noureddine, Ahmed Fawaz, and William H. Sanders. 2017, An Unsupervised Multi-Detector Approach for Identifying Malicious Lateral Movement. In Proc. IEEE 36th Symposium on Reliable Distributed Systems pp. 224-233.

## Slide 21: Challenges in Providing Cyber Resiliency
Adaptation inherently increases the attack surface of a system
Monitoring is essential and increasingly possible, but creates a data deluge that makes difficult to identify relevant attack indicators
Monitors are corruptible, which makes knowledge about the cyber state of the system only partially trustworthy
A world model is needed to reason about indicators, but this reasoning is fallible if an attacker can work outside the model
Catastrophic failures are (hopefully) rare, but can have a huge impact. Predictions based on historical data are notoriously bad at coping with rare events.

## Slide 22: Cyber Security Facts (according to Sanders)
Grid cyber infrastructures are complex, and their complexity will only continue to increase.
Cyber infrastructures intended to be secure must operate through attacks.
Absolute cyber security is unattainable.
Resiliency is imperative: Protect the best you can, but realize that perfect protection is impossible, so resiliency can only be achieved through tolerating attacks through online detection and response.
Assessment of the “amount” of security that a particular resiliency approach provides is essential.

## Slide 23: Failure to Comply with NERC/CIP Requirements: Real Financial Penalties
http://www.nerc.com/filez/enforcement/Public_FinalFiled_NOP_NOC-1448.pdf

## Slide 24: Industrial Control System Network Vulnerability Analysis with NP-View

## Slide 25: Industrial Control System Network Vulnerability Analysis with NP-View

## Slide 26
Hacker, Foreign Gov.
Insider Engineer
Hostile Org.
Insider Engineer
Insider Technician, Insider Operator
Preview of ADVISE Analysis Results

## Slide 27: Engineering in Cyber Resilience: Making Sound Design Choices

## Slide 28: Cyber Security Facts (according to Sanders)
Grid cyber infrastructures are complex, and their complexity will only continue to increase.
Cyber infrastructures intended to be secure must operate through attacks.
Absolute cyber security is unattainable.
Resiliency is imperative: Protect the best you can, but realize that perfect protection is impossible, so resiliency can only be achieved through tolerating attacks through online detection and response.
Assessment of the “amount” of security that a particular resiliency approach provides is essential.

## Slide 29: Cyber Resilient Energy Delivery Consortium (CREDC)
Will improve the resilience and security of the cyber networks that serve as the backbone of energy infrastructure
11 universities and national laboratories: Argonne, Arizona State, Dartmouth, MIT, Oregon State, PNNL, Rutgers, Tennessee State, Univ. Houston, and Wash. State
Funded by DOE: $28.1 million initiative
Led by David Nicol, with Sanders and Sauer as co-PIs
Broadens TCIPG research scope to include the oil & gas industry and provides focus on resiliency

## Slide 30: Final Thoughts
Problem of immense societal importance: “Keeping the lights on”
Absolute cyber security is unattainable
System resiliency is the path forward
Incredible opportunity for academics, rich with opportunity for algorithms and analysis
  Can make progress by solving parts of the problem
Must deeply engage academia, industry, and government